## Slide 1
ACTIVE RADAR · BEGINNER SERIES
01
Radar intuition
and baseline parameters
Transmit briefly. Listen carefully. Turn echo delay into distance.
TX
LISTEN

## Slide 2
ACTIVE RADAR · NOTEBOOK 00
02
Four ideas anchor the lesson
01
Pulse radar
Send a short burst, then stop transmitting.
02
Listening window
Give a distant echo time to return.
03
Duty cycle
Measure the fraction of time spent transmitting.
04
Delay → range
Convert round-trip travel time into distance.

## Slide 3
ACTIVE RADAR · NOTEBOOK 00
03
One baseline connects every lesson
Quantity
Value
Physical role
Carrier frequency
2.45 GHz
Wavelength and later Doppler
Bandwidth
5 MHz
Pulse-compressed range resolution
Pulse width
20 μs
Duration of each transmitted burst
PRI
1 ms
Time available before the next pulse
Sampling rate
20 MHz
20 million recorded samples per second
Target range
1,000 m
Concrete delay-to-range example

## Slide 4
ACTIVE RADAR · NOTEBOOK 00
04
Pulse radar alternates speaking and listening
The antenna sends power during a short burst, then becomes a receiver for the remainder of the cycle.
LISTEN FOR THE ECHO
TX · 20 μs
980 μs
One pulse repetition interval = 1 ms

## Slide 5
ACTIVE RADAR · NOTEBOOK 00
05
The quiet interval makes range measurable
A weak returning echo cannot compete with the outgoing transmit signal.
The radar stops speaking so it can hear. The pulse width is the transmit interval; the rest of the PRI is the listening window.
DUTY CYCLE
D = pulse width / PRI
ROUND-TRIP RANGE
R = c × echo delay / 2
Divide by two: the energy travels out and back.

## Slide 6
ACTIVE RADAR · NOTEBOOK 00
06
Longer PRI means more listening—not more transmitting
COMMON MISREAD
“A longer interval means the radar transmits more often.”
PHYSICAL RESULT
The pulse stays 20 μs. The listening window grows, so duty cycle falls.
Delay is not a technical detail—it is the measurement.

## Slide 7
ACTIVE RADAR · NOTEBOOK 00
07
Pulse radar is a timing instrument
TRANSMIT
Create a precisely timed event.
LISTEN
Wait for reflected energy.
TIME THE RETURN
Use the delay as a distance measurement.

## Slide 8
ACTIVE RADAR · NOTEBOOK 00
08
The measurement happens while the radar listens
20 μs
Transmit: the radar speaks
980 μs
Listen: the echo can return
1 ms
One complete PRI
The listening window is not idle time. It is where the measurement actually happens.

## Slide 9
ACTIVE RADAR · NOTEBOOK 00
09
The radar transmits only two percent of the time
20 μs ÷ 1 ms = 0.02
Duty cycle asks what fraction of each interval is spent transmitting.
2% TX
98% LISTEN

## Slide 10
ACTIVE RADAR · NOTEBOOK 00
10
Delay becomes range through a round trip
1,000 m
Target range
6.67 μs
Round-trip delay
133
Recorded samples
996.8 m
Quantized estimate
R = c × delay / 2
The 3.2 m gap is sample quantization: the true delay falls between two recorded sample boundaries.

## Slide 11
ACTIVE RADAR · FOUNDATION COMPLETE
11
Transmit. Listen.
Time the return.
Careful timing turns an echo delay into a physical measurement with meaning.
2%
TRANSMIT
98%
LISTEN
133
SAMPLES